A note on the L network
The L network is built from series switched inductors wound on toroids and parallel switched capacitors. A relay switches the shunt capacitors between the input or output side of the inductors.
With the large numbers of inductors, capacitors and relays a fair bit of physical space is needed to accommodate them making it impossible to avoid long leads plus the associated contact resistance, stray inductance and capacitance. The net result of this being that you never see exactly the value of the inductor/s or capacitor/s which have been switched in but instead their values plus strays. Further errors in the reactances occur due to toroid values being limited to one turn boundries and the difficulty of obtaining high voltage capacitors leading to having to accept values which do not have a binary progression. To some extent capacitors can be built from series and parallel connection e.g. nominal 5 pF can be built from 4 x 22pF in series and 10pF from 2 in series and finally 1 x 22pF giving 3 nice binary steps but for the next one the closest practical choice is 47pF or 2 paralled 22pF. There is a practical limit on how many capacitors can be paralled together to build larger values as 704pF require 32 x 22pF capacitors in parallel and 1408pF require 64.

Simple tuning algorithms operate under the constraint of any reactance (capacitor or inductor) when switched into the circuit on its own must be greater than the sum of the reactances preceeding it. e.g. L5 must be greater than L1+L2+L3+L4 etc. This is necessary so that when the software commands an increase or decrease of a reactance it must assume this did occur and the opposite did not in fact happen. However due to strays and tolerences mentioned the chances of this happening are unreliable at best and when it occurs the tune will stop with best match assumed when in fact continuing will give further improvement.

An algorithm has been developed to look ahead and see if a better match exists beyond the current indicated best match and continue if so.

The coarse tune algorithm
In order to quickly get at a ball park figure and establish a starting point for a fine tune, a coarse tune algorithm is applied. This simply switches each C relay in turn starting at 0 relays up to the 8th relay and at each step, stepping each L relay in turn again from 0 to 8 and recording the SWR in a 2 dimensional array. There will be a total of 81 readings ( 0 to 8 inclusive for C, by 0 to 8 inclusive for L). The array is examined to retrieve the best SWR and the relay combination is recorded.

The process is done with the capacitors connected to the antenna or output side of the inductors (HiZ) and repeated with the capacitors connected to the input side of the L network (LoZ). The best SWR from each of the two sets of readings is returned and the best of the two determine the starting point of the fine tune and whether we are HiZ or LoZ.

doRelayCoarseSteps(): Caps are connected to Output (HiZ)
bestC = 7; bestL = 1; SWR = 1.50267
fig w
The chart in fig w is a printout of the values obtained from sweeping the capacitor and inductor relays. As can be seen there are some pretty wild swings of SWR over the relay ranges but there is always one spot which is better than the others. In this case it occurs when C relay number 7 is operated along with L relay number 1 giving an SWR of 1.50267. This is a close enough point for us to perform a fine tune without too many relay steps to get our match. These values and the following fineTune values are actual vaues returned from the debug output of my tuner while tuning my 40 Metre antenna.

The fine tune algorithm
A snapshot of the SWR's returned by operating the consecutive relays steps around the chosen best relays from the coarse tune subroutine is shown in fig x. The coarse tune subroutine has returned the best single Inductor and Capacitor relay combination. Holding the Inductor relay fixed the fine tune subroutine is going to traverse the relays around the “best so far” capacitor relay to try to improve the SWR. In the example shown the operated capacitor relay was #7 corresponding to a value of 64 in a binary count (1, 2 , 4, 8, 16, 32, 64, 128) i.e. 7th relay gives a count of 64.

The values array is loaded with the SWR's from the 4 capacitor relay steps each side of the initial relay so it forms a window on the SWR values returned from consecutive relay steps. The value lowRelay is set to hold the relay combination which produced the SWR held in values[0] and is used as a reference to the relay combination needed to get to any array position.

Examining the VSWR data it can be seen that the value returned from the coarse tune subroutine (held in array[4]) is not the best SWR which is actually at relay combination 54 in fig x. The program examines the array to get the SWR trend and returns a count of where the best SWR is which occurs at position, values[0] in this case. If count is less than the reference position i.e. less than (values[4]), the array window is shifted down and if more it is shifted up. In each case the shift is tested to ensure that the array won't extend beyond 0 relay count or 255 relay count.

fig x

The reason for the complexity in this algorithm is that due to tolerance spreads in inductor and capacitor values the total reactance does not smoothly progress as the relays increment or decrement. This particularly shows up when stepping from values like 63 to 64 where several relays change as 64 = relay 7 operated but 63 = relays 1+2+3+4+5+6 operated. If the SWR values in fig x were simply examined each side of relay 64 looking to see if they were greater or less, it would suggest that the value at 64 was the dip. However this is not the case and the true low SWR is at relays 49 (off the scale shown in fig x) so the best SWR would not have been obtained by simply examining the relay each side of the initial best value. By looking further on each side, it is possible to accurately pick up an SWR trend in spite of the capacitor or inductor tolerances.

The window of SWR values held in the values[9] array is simply moved in the direction of best swr until array[4] holds the lowest SWR and the relay combination to produce this becomes the tune setting. The effect of traversing the relays is shown in fig y and it can be seen that as the lowRelay is stepped down the chain the SWR's in values[4] is falling. The value “cnt” refers to the array position holding the smallest SWR and if less than 4 we traverse down and if greater than 4 we traverse up. The limit is reached when the lowest SWR occurs at values[4] and we are then tuned.

fig y
After tuning the capacitors, the same process is repeated for the inductors and then back to the capacitors again etc. until no further improvement can be obtained. It should be noted that sometimes changing say the inductors, will cause the capacitors to back up a little over changes just made to them and vice versa but eventually equilibrium is reached.